## Slide 1
PE / PXA / PLA
What the SMD spatial workflows do in eTitles
Plan Examination • Compute/Compare • Plan Annexation
1
SUBMITTED
SURVEY
PDF / CAD / coordinates
2
COMPUTE
technical QA
3
COMPARE
cadastral QA
4
PLA
authoritative link
PM focus: one controlled path from submitted survey → validated geometry → authoritative parcel/title link.

## Slide 2
SMD in the eTitles transaction lifecycle
Innola orchestrates the workflow; ArcGIS Pro executes the GIS work; ArcGIS Enterprise holds authoritative spatial data.
IN
Customer / LTD
submission starts
WF
eTitles / Innola
transaction control
GIS
SMD / ArcGIS Pro
compute + compare
DB
ArcGIS Enterprise
CadMap • CadIndex • PF
OK
eTitles result
decision + audit
Key point
PE/PXA and PLA are stages within a transaction-controlled SMD spatial process, with every action linked back to the eTitles record.
One transaction record, one spatial workspace, one auditable execution path.

## Slide 3
PE / PXA in one picture
The Plan Examination process is easiest to explain as two questions: Compute and Compare.
INPUTS
Survey plan PDF
DWG / DXF CAD
Computer sheet
PE number
COMPUTE
Is the submitted survey internally and mathematically correct?
✓ Required plan elements
✓ Coordinate/geometry build
✓ Closure calculation
✓ Bearing & distance checks
✓ Topology validation
COMPARE
Does the validated survey agree with the existing cadastre and records?
✓ Overlay on CADMAP/CADINDEX
✓ Check adjacent owners
✓ Detect overlaps/conflicts
✓ Use supporting records
✓ Prepare examiner findings
Compute validates the survey itself; Compare validates the survey against the authoritative cadastral environment.

## Slide 4
Compute stage — from submission to validated geometry
The Compute stage transforms the submitted survey into a structured GIS workspace, then validates its technical integrity before Compare.
1
LODGMENT
Create transaction workspace and load plan/CAD/computer sheet.
2
STRUCTURE CHECK
Confirm required content, layers, coordinates and usable survey structure.
3
GEOMETRY CHECK
Validate traverse, closure, bearings, distances, directions and tie lines.
4
TOPOLOGY & INTEGRITY
Confirm point-line connectivity, duplicates and valid geometry.
5
DIGITAL CONSISTENCY
For digital submissions, confirm CAD and PDF represent the same survey.
6
RESULT & REVIEW
Compile findings; examiner confirms outcome before Compare.
A. Validate Structure
Is the submitted survey complete and correctly structured for computation?
✓ Required plan elements present
✓ Coordinate / control information available
✓ Expected CAD layers / features present
✓ Computer sheet and plan data can be interpreted
✓ Spatial reference / JAD2001 context confirmed
B. Validate Geometry
Is the survey mathematically and geometrically correct?
✓ Build points and boundary lines
✓ Traverse / closure within tolerance
✓ Bearings and distances match submission
✓ Line directions are correct
✓ Tie lines / referenced control points validate
C. Validate Integrity
Is the GIS geometry internally consistent and ready for Compare?
✓ Points correspond to line endpoints
✓ No duplicate points or boundary lines
✓ Valid connectivity / no structural breaks
✓ CAD vs PDF consistency where applicable
✓ Record warnings, failures and examiner comments
COMPUTE OUTCOME
Validated geometry + structured findings + examiner decision → ready for COMPARE or returned for correction.

## Slide 5
PLA — Plan Annexation after approval
PLA links the approved plan to the authoritative cadastral and title environment.
1
Approved Plan
Final PE outcome
2
RT Examination
legal/spatial readiness
3
Parcel Fabric Update
create/update authoritative parcel
4
Plan Annexation
link plan to parcel/title
5
eTitles / LTD
return status and audit
Simple PM explanation
PE validates the survey. PLA makes the approved survey operational by connecting it to the authoritative parcel fabric and the title/registry process.
PLA is the bridge from approved survey plan to authoritative parcel-title relationship.

## Slide 6
Management value: why the workflows matter
The value is less about a tool and more about controlled, repeatable, auditable spatial processing.
C
Consistency
Same structured steps for every comparable transaction.
T
Traceability
Every spatial action tied to transaction ID, user, time and output.
Q
Quality
Systematic geometry, topology, closure and conflict checks.
I
Integration
SMD, LTD, valuation and records operate through one workflow backbone.
Executive takeaway
PE/PXA/PLA create a controlled chain from submitted survey to validated geometry to authoritative cadastral/title update.